## Slide 1: Quantum Sensor Design with Multiphysics Simulation
Peter Hobson
Physics PhD Student University of Nottingham
Richard Chippendale
Technical manager
COMSOL

## Slide 2: Agenda
Simulating with COMSOL Multiphysics®
Introduction to the Electromagnetic Branch
Quantum Sensor Design
Q&A Session
Next Steps and Further Resources
Notes: SHORT
Multiphysics software platform
  Real-world designs and processes in a virtual environment
Option to work directly with equations
  Makes customization easy
Application Builder
  Quickly turn your models into specialized apps
  Application = physics model + user interface
LONG
To realize the full benefits of simulations (such as shorter product development times, greater insights, more innovative designs, ability to reject flawed concepts early, etc.) models need to account for all the physics that affect the outputs they are trying to predict. In other words, if you ignore some important physics, your model is not going to be high fidelity. And many, probably most, systems that engineers analyze involve multiple physics. For instance, if you want to predict how hot a laptop gets, you may need to consider chemical reactions in the battery, Joule heating in electrical components, air flow affecting cooling, etc. It's not just a heat transfer equation you need to solve to get accurate predictions. And that's the whole idea, the whole philosophy of COMSOL Multiphysics: it enables the modeler to combine arbitrary physics together, no matter how intricately they may be coupled, and to build powerful, flexible, accurate models. The software even allows you to add your own equations, should it be necessary.
A major innovation of COMSOL Multiphysics is the Application Builder. The Application Builder is the tool that lets you turn your sophisticated model into an easy-to-use app that your colleagues and customers who are not into modeling can use. This enables them to contribute to the analysis process.

## Slide 3: COMSOL Multiphysics®
Notes: SHORT
Multiphysics software platform
  Real-world designs and processes in a virtual environment
Option to work directly with equations
  Makes customization easy
Application Builder
  Quickly turn your models into specialized apps
  Application = physics model + user interface
LONG
To realize the full benefits of simulations (such as shorter product development times, greater insights, more innovative designs, ability to reject flawed concepts early, etc.) models need to account for all the physics that affect the outputs they are trying to predict. In other words, if you ignore some important physics, your model is not going to be high fidelity. And many, probably most, systems that engineers analyze involve multiple physics. For instance, if you want to predict how hot a laptop gets, you may need to consider chemical reactions in the battery, Joule heating in electrical components, air flow affecting cooling, etc. It's not just a heat transfer equation you need to solve to get accurate predictions. And that's the whole idea, the whole philosophy of COMSOL Multiphysics: it enables the modeler to combine arbitrary physics together, no matter how intricately they may be coupled, and to build powerful, flexible, accurate models. The software even allows you to add your own equations, should it be necessary.
A major innovation of COMSOL Multiphysics is the Application Builder. The Application Builder is the tool that lets you turn your sophisticated model into an easy-to-use app that your colleagues and customers who are not into modeling can use. This enables them to contribute to the analysis process.

## Slide 5: Modeling Regimes
http://www.comsol.com/blogs/computational-electromagnetics-modeling-which-module-to-use/

## Slide 6
Quantum Sensor Design with Multiphysics Simulation
Peter J Hobson

## Slide 7: About me
Peter J Hobson peter.hobson@nottingham.ac.uk
Researching analytic formulations of magnetic fields.
Python and COMSOL Multiphysics® to design and simulate magnetic field coils.
Improve sensors for brain scanning, gravity measurement, timing, and much more.

## Slide 8: This webinar
Quantum sensors
Magnetic shielding
Coil design inside magnetic shields
Simulation using COMSOL®
Two live demonstrator models
Numerical simulation
Real world

## Slide 9
Quantum sensors

## Slide 10: 20th century quantum technologies
Many existing technologies:
GPS
lasers
semiconductors
MRI
work because of quantum physics
Sir Peter Mansfield – Nottingham – 2003 Nobel Prize
Left school at 14
Some colleagues asked “but is it physics?”
500,000,000 people have had MRI scans

## Slide 11: 21st century quantum technologies
New quantum technologies are being developed:
computing & information
cameras
quantum cryptography
[1] F. Arute et al. Nature 574, 505–510 (2019); [2] G. Musarra et al. Phys. Rev. Applied 12, 011002 (2019); [3] J. Yin et al. Nature 582, 501–505 (2020).
[1]
[3]
[2]

## Slide 12: 21st century quantum sensors
New quantum technologies are being developed:
magnetometers for healthcare (OPMs)
In 2015, neurological disorders accounted for:
10.2% of global disability adjusted life years lost
16.8% of all global deaths
Dementia prevalence is rising; the number of people living with dementia worldwide will reach 75 million by 2025.
[4]
[4]
[4] E. Boto et al. Nature 555, 657–661 (2018).
Resolution
flexibility

## Slide 13: 21st century quantum sensors
New quantum technologies are being developed:
atom interferometers for gravity sensing
In 2014–15, utility street works incurred costs of more than £1.5 billion to UK government. The cost of these street works to the UK economy was estimated around £7 billion.
[5] K. Bongs et al. Nat. Rev. Phys. 1, 731–739 (2019) (please see for individual figure references).
navigation
testing fundamental physics
[5]

## Slide 14: Anatomy of a quantum sensor
Creation, control, and measurement of quantum states:
Using superposition and entanglement
Cold atoms require specific environments:
  new materials & architectures
  design optimization
  advanced manufacturing
  magnetic field control
Design
optimization
New
manufacturing
techniques
New
materials &
architectures

## Slide 15: Unwanted magnetic fields
Magnetic fields:
Limit the temperature of atomic clouds cooled by optical molasses[6].
Induce a bias in atomic clocks[7].
Cause gravity sensors to be sensitive to the Coriolis force[8] or the quadratic induced Zeeman effect[9].
Limit the resolution of magnetometers for healthcare.
[6] P. D. Lett et al. J. Opt. Soc. Am. B 6, 560 (1989); [7] L. Liu et al. Nat.. Commun 9, 2760 (2018);
[8] B. Wu et al. Opt. Express 27, 11252 (2019); [9] B. Wu et al. Metrologia 51, 452 (2014).
[9]
The Earth produces a magnetic field of (30–60) μT!

## Slide 16
Magnetic shielding

## Slide 17: Passive magnetic shielding
[10] S. Celozzi, R. Araneo, and G. Lovat, Electromagnetic Shielding (John Wiley & Sons, Ltd, 2008) pp. 282–316.
Electromagnetic shielding has been of interest for many years:
  power transformers
  cathode ray tubes
  electric batteries
In the magnetostatic regime, enclose a region in a material, & divert flux away from the shielded region (flux shunting).
High-frequency fields cancelled by eddy currents.
[10]
Lower density of flux lines

## Slide 18: Passive magnetic shielding
Materials with high magnetic permeability provide a low-resistance pathway for lines of magnetic flux.
Mu-metal is the industrial standard shielding material.
Cylindrical geometries are widely used due to their comparatively high shielding factor relative to their low manufacturing cost.

## Slide 19: Passive magnetic shielding
We quantify shielding by considering the shielding efficiency:
Multiple layers of shielding material improve the shielding factor.
Without shielding
With shielding
[10]

## Slide 20: Passive magnetic shielding
Analytical models of magnetic shielding factors require approximations, such as infinitely long cylinders/infinite magnetic permeability.
Experimental testing is expensive, laborious, & systematic errors must be carefully controlled.
COMSOL Multiphysics® is a powerful tool for rapid testing and optimization of magnetic shielding:
  quick
  flexible
  intuitive

## Slide 21: Simulating magnetic shields in COMSOL Multiphysics®
Closed cylindrical magnetic shield made of mu-metal:

## Slide 22: Simulating magnetic shields in COMSOL Multiphysics®
Apply a transverse magnetic field & simulate the shielding factor:
COMSOL notes:
‘Magnetic Fields, No Currents’ (mfnc)
AC/DC and LiveLink™ for MATLAB® modules
Magnetic shielding at the cylinder boundary
Magnetic insulation surrounds the Universe
‘Infinite Element Domain’[11]
Let’s do this in COMSOL®!
[11] https://uk.comsol.com/blogs/how-to-choose-between-boundary-conditions-for-coil-modeling/

## Slide 23: Checking our results
Agrees with a theoretical model (infinitely long cylinder)[10]:

## Slide 24
Coil design inside cylindrical magnetic shields

## Slide 25: Active field coils and passive magnetic shields
Active coil system
Passive magnetic shield

## Slide 26: Active field coils and passive magnetic shields
Active coil system
Mu-metal shield
Fields are required for quantum sensors (quantization axis / positioning in MOTs)
Cancel different fields in a targeted region
Current driver systems
Distorted by passive shielding
Cheaper than optimized field coils
Greater shielding efficiency with multi-layer shields
Bulky and heavy
Degaussing to remove residual magnetization
Entry and exit holes reduce shielding efficiency

## Slide 27: fields_in_shields
Unless we combine the two![12]
[12] M. Packer et al. Phys. Rev. Appl. 14, 054004 (2020). Designs generated using our Python module fields_in_shields. Patented for commercial use.

## Slide 28: fields_in_shields
Designs generated using our Python module fields_in_shields.
Solved using Green’s functions.
Generates a solution representing a continuum of current flowing on an interior open cylinder.
Generate any arbitrary magnetic field.
George Green:
Nottingham Victorian miller–mathematician

## Slide 29: fields_in_shields
Shielded Analytic
Experimental Data
Experimentally verified.
Generate uniform transverse field to 1 part in 1000 accuracy over desired region.
Designs generated using our Python module fields_in_shields.
Rolled into a cylinder
COMSOL® experiment simulation
COMSOL® analytic simulation

## Slide 30: Simulating active–passive systems in COMSOL Multiphysics®
Implementation:
Analytical
Continuum
Discrete

## Slide 31: Simulating active–passive systems in COMSOL Multiphysics®
Simulate an active–passive system:
COMSOL notes:
‘Magnetic Fields’ (mf)
Magnetic shielding at the cylinder boundary
Magnetic insulation surrounds the Universe
Surface current density uses in-built functions on COMSOL® and Fourier coefficients calculated from fields_in_shields
Let’s do this on COMSOL®!

## Slide 32: Checking our results
These fields match the analytic model to 1 part in 50000[12].
We can generate any arbitrary field profile, and rapidly test it using COMSOL®.

## Slide 33: Bespoke design using COMSOL Multiphysics®
1. Perfect magnetic conductor approximation
2. Entry/exit holes
3. Discrete wire patterns
Finite thickness and magnetic permeability

## Slide 34: 1. Perfect magnetic conductor approximation
Intrinsic error in the coil
COMSOL simulation
The error in the field uniformity reduces as the shield thickness increases. By d=1 mm the error is negligible[12].

## Slide 35: 2. Entry/exit holes
The error in the field uniformity increases as the shield holes get larger. At ⍴h/⍴s =0.25 the error is negligible[12].
Error with no holes
COMSOL simulation

## Slide 36: 3. Discrete wire patterns

## Slide 37: 3. Discrete wire patterns
Simulate discrete active–passive systems to calculate discretization error:
COMSOL notes:
‘Magnetic Fields’ (mf)
Magnetic shielding at the cylinder boundary
Magnetic insulation surrounds the Universe
Wire patterns use edge currents along interpolation curves
Matches analytical model to 1 part in 10000!

## Slide 38: Moving forward
Implement into design of quantum sensors
Design coils on other geometries
Design coils for high-frequency field cancellation
Rapid prototyping in COMSOL®
COMSOL and COMSOL Multiphysics are registered trademarks of COMSOL AB.

## Slide 39: Thank you for listening!
Nottingham theory (Michael Packer, Kate Clements, Alister Davis, Mark Fromhold)
Sir Peter Mansfield Imaging Centre (Niall Holmes, Jim Leggett, Paul Glover, Matthew J Brookes, Richard Bowtell, and many more)
Quantum Technology Hub Sensors and Timing partners (Jamie Vovrosh, Ben Stray, Jonathan Winch, Michael Holynski, Kai Bongs, and many more)
Magnetic Shields Limited
Many more …
Mike
Mark
Kate
Ali
Me
peter.hobson@nottingham.ac.uk

## Slide 40: Q & A
Inductor 3D model surrounded by Infinite Elements
3D Permanent Magnet Motor

## Slide 41
uk.comsol.com/contact