## Slide 1
Institute for Chemical Reaction Engineering
Floating Green Hydrogen Production: LOHC as an energy transport vector
EKC 2023
Andreas Bösmann
Friedrich-Alexander Universität Erlangen-Nürnberg
Andreas.boesmann@fau.de

## Slide 2
Head of Institute
Prof. Dr. P. Wasserscheid
Tel. 09131-85 27420
Fax. 09131-85 27421
peter.wasserscheid@fau.de
Advanced catalytic systems and processes; LOHC and clean hydrogen technologies
Group leaders Wasserscheid team
Academic Staff of the CRT
Dr. P. Schulz
Ionic Liquids
Dr. A. Bösmann
Hydrogen
and Energy
Dr. M. Haumann
Hybrid materials
Further Professors
Prof. Dr. T. Franken
Catalytic and electrocatalytic systems and processes
Dr. P. Schühle
Catalytic systems for chemical energy storage
Dr. A. Inayat
Green porous materials

## Slide 3
What is a suitable energy vector for offshore wind power?
Energy transport?
Current technology: Cable connection to land-based grid.
Consumes up to 50 % of total CAPEX.
No energy storage included.
Are there other options?

## Slide 4: What makes hydrogen so interesting?

## Slide 5: Can hydrogen be made feasible offshore?
Transport options for hydrogen
from offshore installations:
Method | Pro | Con
Pipeline | Highly efficient | Cost prohibitive
Compressed/Cryo | Established technology | Safety aspects Compression/cooling energy
Metal hydrides | Low pressure storage | Solid handling Weight (1,5 wt% H2 capacity) Incompatible with water
LOHC | Ambient storage Liquid handling | Heat demand for H2-release

## Slide 6: Liquid organic hydrogen carriers
H2
H2
Hydrogenation
Dehydrogenation
High storage density
Large liquid temperature range
Reversible storage
Compatible with liquid infrastructure
Catalyst
Catalyst
Substance A
Substance A
Substance B

## Slide 7
Hydrogen storage capacity (kg H2 / kg (liter) LOHC system)
Reversibility of the charging/decharging process (thermodynamics)
Rate of charging/decharging (kinetics)
Selectivity and stability
Liquid range of carrier fluid
Compatibility to today‘s infrastructure for fuels
Safety aspects
Toxicology and ecotoxicology
…
?
Selection of a most suitable LOHC System

## Slide 8
54.5 kg/m3 H2
Liquid range: -35 °C – 270 °C
Compatible with today‘s infrastructure for fuels
Non-flammable
GHS: 7, 8, 9
BT
Selection of a most suitable LOHC System
(Perhydro)-Benzyl-Toluene

## Slide 9: „LOHC 3.0“: Benzyltoluene
6 H2
6 H2
Hydrogenation
Dehydrogenation
100 – 320 °C
> 10 bar H2
> 240 °C
< 10 bar H2
6,2 wt% H2 ≙ 2,1 MWh/t
m.p. -35 °C, b.p. 270-290 °C
Exothermic hydrogenation: 63.5 kJ/molH2
Ru, Rh, Pd or Pt
Pt

## Slide 10: LOHC – a particularly safe way of hydrogen storage

## Slide 11: Industrial projects
ChemPark Dormagen:
1800 t/a H2 hydrogenation capacity
heat integration into ChemPark
Rotterdam:
600 t/a H2 dehydrogenation capacity
Hydrogen Fuel station Erlangen (since 2022):
Public fuel station for 700 / 350 bar H2

## Slide 12: Aspects of the LOHC technology development
Nanoscale:
Optimizing the
active catalytic site
Mesoscale:
Optimizing mass transfer at the catalyst pellet level
Operando spectroscopies, microscopies, on-line monitoring
Reactor scale:
Optimizing mass and heat transfer
Storage unit scale:
Optimizing heat integration aspects
Theory & simulation:
DFT, CFD, mass & heat balances
Preuster, Papp, Wasserscheid, Accounts of Chemical Research, 2017, 50(1), 74-85.
General: Design and test other LOHC systems

## Slide 13: Reactor Development: Main obstacles
Hydrogenation
Operating window: 100 – 320 °C, 10 – 50 bar hydrogen pressure
Heat transfer (cooling) is limiting
Well-known process in industry
Hydrodynamics of packed bed reactors under motion?
Operation under offshore-conditions?
Dehydrogenation
Operating window: 250 - 320 °C, 0.5 – 5 bar
Side reactions, degradation/deactivation of LOHC and catalyst
Heat- and mass transfer problems
Liquid-phase gas-generating processes are not well-known

## Slide 14: Reactor Development: Hydrodynamics
Hydrogenation
Vertical packed-bed tubular reactor
First experiments indicate permanently tilted reactor tubes are detrimental to reactor efficiency
Possible fluid stratification in catalyst bed
Optimal fluid distribution
Stratification, loss of efficiency
?
Unknown behavior of fluids under oscillating movement.

## Slide 15: Plant Development: Fault resistance
Typical industrial hydrogenation plant:
Embedded in industrial site with complete infrastructure
24/7/365 operators present
Offshore hydrogenation plant:
Nothing of the above
Development goals:
Remote operability
Fault resistance, resilience

## Slide 16: LOHC as transport medium
Estimates for a 15 MW wind turbine with LOHC-storage:
Electrolyzer (η ~ 0.6) at 15 MW generates 270 kg/h H2 (6.48 t/d)
270 kg H2 is stored in 5.4 m3 LOHC
Storing 270 kg H2 releases 2,5 MWh heat at hydrogenation temperature
Monthly LOHC use: ~ 3.900 m3
Monthly water use: ~ 1.800 m3
Catalyst volume: ~ 3 m3
Heat for desalination for 1.800 m3 (multiple effect distillation): ~ 15 MWh

## Slide 17: Thank you for your kind attention
Dr. Andreas Bösmann
Friedrich-Alexander-Universität Erlangen Nürnberg
Institute of Chemical Reaction Engineering
Egerlandstr. 3, 91058 Erlangen, Germany
andreas.boesmann@fau.de
www.crt.tf.fau.de
Picture: CRUSE Offshore GmbH