## Slide 1: Network in Belle II
Dr. Silvio Pardi
On behalf of Belle II Computing Group
CHEP19 – Adelaide Australia
07/11/2019

## Slide 2
26 Countries/regions
~120 Institutions
~1000 Colleagues

## Slide 4
KEK T0

## Slide 5: Network Links: SINET 100G RING
JP-EU link upgrade from 2x10G to 1x100G -Feb. 2019 (Tokyo to Amsterdam on NetherLight + L3 Peering GEANT-SINET)
JP-NY link replaced by LA-NY 100G link . March 2019
New Trans-Atlantic NY-EU 100G March 2019
https://www.nii.ac.jp/news/release/2019/0301.html
meetings.internet2.edu/media/medialibrary/2019/03/07/20190307-nakamura-SINET.pdf
https://www.geant.org/News_and_Events/Pages/100Gbps-ring-connection-around-the-globe-supercharges.aspx

## Slide 6: Belle II Network
Belle II
Belle II
Belle II
Belle II
Belle II
30% Sites on LHCONE (including KEK)
70% Sites General IP
5 Sites on LHCOPN
All RAW Data Centers are on LHCONE
More than 80% of Storage on LHCONE
More than 80% of Computing Power
on LHCONE

## Slide 7
Network Data Challenge activity started in 2015.
FTS Jobs From KEK to the candidate RAW Data Center.

## Slide 8
Data Challenge 2018/2019 via FTS Jobs
35 Gbps 2019
35 Gbps 2018
21Gbps 2018
35 Gbps 2019
To be test
KEK vs EU sites
KEK vs BNL
KEK vs UVIC
14 Gbps
21 Gbps

## Slide 9
Network Data Challenge KEK vs EU (May 2019)
KEK-> EU (FTS job with multiple destinations
CNAF,DESY, KIT, IN2P3, Napoli and SIGNET)
Max 35.83 Gbps with 16 streams
EU->KEK (FTS job with multiple source
CNAF,DESY, KIT, IN2P3, Napoli and SIGNET)
Max 34.87 Gbps with 16 streams

## Slide 10
DTN service run on a server optimized to send and receive data at 100Gbps without system bootleneck.
It’s equipped with an array NVME SSD 8 lane PCI-e 3.0
And multiple 100G NIC.
It’s connected directly on the network without firewall.
Tools installed
•Fast Data Transfer Service (FDT)
•GridFTP
•Udpmon
•Iperf (v2.0.8)
•Iperf3 (v3.1.2)
Network Data Challenge KEK vs EU via DTN by GEANT
161ms RTT
DTN
100Gbsp
kek-storm01
4x10Gbsp
100 Gbps Link

## Slide 11: Iperf3 tests done in September KEK vs DTN
Mostly used the DTN server in London (100Gbps)
Server accessible via LHCONE
DTN worked as server running 20 iperf3 instances on port 5001-5020.
Client on kek2-storm01 and kek2-storm02 (4x10Gbps)
- Single process from 1 to 128 streams
- Multiple processes with 16 and 32 streams
Thank you to Go-san and Suzuki-san for perform the tests.

## Slide 12: Analysis of iperf3 performance from kek2-kek2-storm01 vs London DTN
With a number of streams fixed at 16. Increasing the number of processes bandwidth peak linearly increases up to 37Gbs
Chart: Parallel processes of 16 streams each vs Gb/s
| 1 | 2 | 3 | 10 | 20
1 2 3 10 20 | 2 | 4 | 6 | 20 | 37

## Slide 13: 10 processes x 32 streams Max 37Gbps – Average 32Gbps
20 processes x 16 streams
Up to 37Gbps – Average 32Gbps
KEK -> DTN

## Slide 14: Network Monitoring
Tools provided by Data Centers
Graphs provided by Network Operators
Perfsonar Mesh
FTS Monitoring
Internal Tools integrated in DIRAC

## Slide 15: Network Monitoring KEK (LHCONE)

## Slide 16: BNL vs SINET – Last 2 months
SINET - BNL TRAFFIC

## Slide 17: LHCONE-SINET Peering GEANT-SINET Peering CANARIE - LHCONE-KEK TRAFFIC

## Slide 18: Perfsonar MADDASH of RAW Data Centers
Belle II RAW Data Centers IPv4 Throughput
Belle II RAW Data Centers IPv4 Latency

## Slide 19: Conclusion
Belle II experiment has started data taking and is working to reach the maximum luminosity in the coming years.
International links are improving the connectivity of KEK vs the RAW Data Centers in EU, USA and Canada.
A yearly activity of Network Data Challenge is established.
Network Monitoring is done from different points of observation.

## Slide 20: Some of the people involved in different aspects of Network Data Challenge 2018/2019
BNL (Hiro Ito)
CNAF (Lucia Morganti, Stefano Zani, Vladimir Sapunenko)
DESY (Andreas Gellrich)
GARR (Marco Marletta)
GEANT ( Domenico Vicinanza)
IN2P3 (Jerome Bernier, Laurent Caillat, Ghita Rahal, Karim Trabelsi)
KEK (Soh Suzuki, Go Iwai)
KIT (Bruno Hoeft, James Kahn)
RENATER (Laurent Gydé)
SIGNET (Marco Bracko)
UIVc (Marcus Ebert, Robert Taylor, Rolf Seuster)
Perfsonar Team (Shawn McKee, Marian Babik)
Several other people
mailing list belle2-wan-networking@belle2.org (57 members) THANK YOU TO ALL THE PARTICIPANTS

## Slide 21
BACKUP

## Slide 22: Belle II status and next plans
• Phase-3, 2019 Spring Commissioning (Mar.~Jun)
• Recorded integrated luminosity of 6.5 fb -1 was accumulated
•Plans for Next Operation (2019 Oct. ~ 2020 June)
•Goal : Integrated Lumi. of ~200 fb-1 by the summer 2020

## Slide 23
Involved sites KEK, CNAF, DESY, IN2P3, KIT, NAPOLI, SIGENT
15 May 24TB sent in 4h effective - from KEK to EU
17 May 16TB sent in 3h effective - from EU to KEK
KEK-> EU Used a single job with multiple destinations - max 35.83 Gbps with 16 streams
Average 13.5 Gbps
EU->KEK Used a single job with multiple sources - max 34.87 Gbps with 16 streams
Average 11.8 Gbps
Several tests done. Up to 5TB for single job
KEK vs EU Sites

## Slide 24
Current Results vs Estimated Requirements for RAW DATA Movement (Gbps)
 | FROM KEK |  | 
 | DC 2018/19 Peak (Gbps) | Requirement for RAW Data (Average Throughput) Gbps | Goal: 5 X Average Throughput (Gbps)
ITALY (CNAF) | 20.8 | 1.2 | 6
GERMANY (KIT/DESY) | 21 | 1.2 | 6
FRANCE (IN2P3) | 12.4 | 1 | 5
USA (BNL) | 35.5 | 1.8 | 9
CANADA (UVIC) | 13.5 | 1 | 5
KEK to EU | 35.8 | 3.4 | 17
Max KEK in Outbound | 35.8 | 6.2 | 31

## Slide 25: Single iper3 process
Iperf 1 stream 0,16 Gb/s (20MB/s)
Iperf 16 streams 2,17 Gb/s
Iperf 128 streams 10 Gb/s
iperf3 -c $server -p 5001 -T s1 --json -Z -P 128 -t 60 > $prefix-p128s1.json 2>&1
snd_cwnd automatic: 3.3MB

## Slide 26: iperf3 single process performance kek2-storm01 vs London DTN
the bandwidth linearly increases with the number of parallel streams up to 8Gb/s with 64 streams
With 128 streams we saturated one of the 10Gbps NIC of the kek2-storm01
Chart: Parallel Streams vs Gb/s
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128
 | 0.125 | 0.25 | 0.5 | 1 | 2 | 4.2 | 8.3 | 10

## Slide 27
20 processes x 32 streams Max 33Gbps
20 processes x 16 streams
Max 32Gbps
DTN to KEK

## Slide 28
20 Gbps LINK via LONDON
NEW 100Gbps LINK VIA AMSTERDAM
Latency Drop between KEK (JP) perfsonar and KIT (DE) perfsonar from 91ms to 82ms one way

## Slide 30
BNL Peering and Storage network
2x25Gbps
2x10Gbps
2x10Gbps
2x10Gbps
2x10Gbps
2x10Gbps
2x10Gbps
2x10Gbps
2x10Gbps
ESnet
LHCOPN
LHCONE
2x100Gbps
SINET
at LA
LHCONE/OPN
Trans-Atlantic
100Gbps
100Gbps
KEK
Various European Sites
GridFTP Doors
Storage Servers

## Slide 31
Note: The entire system is shared with non LHC VOs
Géant
CNAF Core Switch
SRM Server StoRM
Each link 2x10Gbps
GPFS Storage
2 * FC@16 Gbps each link
GridFTP ds-815
GridFTP ds-915
FC
switch
GARR
KEK – SINET5
100 Gbps
CNAF Peering and Storage (please check) Slide From https://kds.kek.jp/indico/event/25343/session/3/material/1/0.pdf
LHCONE
100Gbps
LHCONE
2x100Gbps

## Slide 32
DESY Peering and Storage
Géant
DESY WAN router
LHCONE
100Gbps
LHCONE/Internet
2*50Gbps
DFN
KEK – SINET5
100 Gbps
DESY Data Center Router
n*10Gbps
soon: 100Gbps
dCache Fileserver
dCache Fileserver
dCache Fileserver
dCache Fileserver
dCache Pool
36*10Gbps (no LHC VOs)
DESY Firewall
DESY
SW
2*10Gbps
2*40Gbps
(all VOs)

## Slide 33
KEK Peering and Storage (please check)

## Slide 34
KIT Peering and Storage (please check) Slide From https://kds.kek.jp/indico/event/25343/session/3/material/1/0.pdf
KEK-SINET
100 Gbps

## Slide 35
IN2P3 Peering and Storage
GEANT
KEK – SINET5
100 Gbps
RENATER
Router
ccpn-inter
LHCONE
40Gbps
LHCONE
4x10 Gbps
dCache Pool
10Gbps
ccpn-coreb
dCache Fileserver
dCache Fileserver
2x100G

## Slide 36
SIGNET Peering and Storage
KEK-SINET
100 Gbps

## Slide 37
Note: The entire system is shared with non LHC VOs
Géant
INFN Napoli Core Switch
LHCONE
100Gbps
DPM Head Node
Each link 1x10Gbps
LHCONE
2*10Gbps
GridFTP ds-815
GridFTP ds-915
GARR
KEK – SINET5
100 Gbps
NAPOLI Peering and Storage
GridFTP ds-815

## Slide 38: Network Data Challenge 2018 Details
Fore each site we tested both drection KEK->SiteX and SiteX-> KEK
Each Test consisted in a set FTS jobs
100x10GB (1TB total)
200x10GB (2TB total)
We used different configuration: 25,50,100 and 200 concurrent files and from 1 to 16 TCP streams in function of the site.
All tests have been done using BNL FTS3 service
Monitoring Tools:
FTS statistics, retrieved every 10 seconds by a local script
Plots provided by Sites from the relative local monitoring systems
Plot from the NREN monitoring system

## Slide 39: Network Data Challenge 2018: KEK-CNAF
FTS Monitoring system
 | From KEK (peak) | To KEK (peak) | From KEK (average) | To KEK (average)
CNAF | 20.8 | 18.1 | 15.3 | 16
KEK->CNAF
CNAF->KEK
20Gbps
20Gbps

## Slide 40: Network Data Challenge 2018: KEK-DESY
FTS Monitoring system
 | From KEK (peak) | To KEK (peak) | From KEK (average) | To KEK (average)
DESY | 15.9 | 16.7 | 10,4 | 11.7
KEK->DESY
DESY->KEK
15Gbps
18Gbps

## Slide 41: Network Data Challenge 2018: KEK-KIT
FTS Monitoring system
 | From KEK (peak) | To KEK (peak) | From KEK (average) | To KEK (average)
DESY | 21 | 22.4 | 13.2 | 12.4
20Gbps
20Gbps

## Slide 42: Network Data Challenge 2018: KEK-KIT
FTS Monitoring system
 | From KEK (peak) | To KEK (peak) | From KEK (average) | To KEK (average)
DESY | 21 | 22.4 | 13.2 | 12.4

## Slide 43: Network Data Challenge 2018: KEK-SIGNET
FTS Monitoring system
 | From KEK (peak) | To KEK (peak) | From KEK (average) | To KEK (average)
SIGNET | 7.3 | 10.0 | 6.7 | 8.5
5Gbps
4.5 Gbps
Single Storage

## Slide 44: Network Data Challenge 2018: KEK-BNL
FTS Monitoring system
 | From KEK (peak) | To KEK (peak) | From KEK (average) | To KEK (average)
BNL | 35.3 | 20.4 | 15,5 | 15,7
CONNECTION - sunn-cr5->pacwave
36Gbps

## Slide 45: Network Data Challenge 2018: KEK-UVIc
FTS Monitoring system
 | From KEK (peak) | To KEK (peak) | From KEK (average) | To KEK (average)
UVIc | 13.7 | 21.9 | 10.5 | 16.6
20Gbps
16Gbps
One of the storage in UVIc

## Slide 46: Summary of Network Data Challenge 2018 Current Results vs Previous Tests (Gbps)
To be completed
 | DC 2018 |  | DC 2013-2017 | DC 2018 |  | DC 2013-2017
 | From KEK (peak) | From KEK (average) | From KEK (peak) | To KEK (peak) | To KEK (average) | To KEK (peak)
CNAF | 20.8 | 15.3 | 18 | 18.1 | 16 | 9.2
DESY | 15.9 | 10,4 | 6 | 16.7 | 11.7 | 11
KIT | 21 | 13.2 | 5.6 | 22.4 | 12.4 | 3.2
BNL | 35.5 | 15.5 | 12 | 20.8 | 15.7 | 12.8
UVIC | 13.4 | 10.5 | / | 21.9 | 16.6 | /
SIGNET | 7.3 | 6.7 | 1.6 | 10 | 8.5 | 3
IN2P3 | Do be done | Do be done | / | Do be done | Do be done | /