## Slide 1: Long-term modelling of electricity market prices to examine prospective revenues of storage agents
Martin Klein, Christoph Schimeczek
DLR Institute of Engineering Thermodynamics – Energy Systems Analysis

## Slide 2: The challenge
Electricity
CO2 emissions
air pollution
 Renewable energy
Wind & PV
non-dispatchable
 Flexibility options
missing reliability
volatile output
When profitable?
What amounts?
Flex options
different timescales
expensive

## Slide 3: The challenge Profitability of arbitrage
German electricity price – a day in 2018
 Shape of price curve important for storage operators
Storage profitability
Block Median: Peak-to-peak
Block hours  Energy-to-power ratio (E2P)
Profitability  price fluctuations

## Slide 4: The challenge Price modelling
Fundamental model REMix
  Linear optimization
  Electricity + sector coupling
  Scope: Europe
  Transport grid restrictions
Cao et al., Sustainability 2018, 10, 1916, doi:10.3390/su10061916
 How to improve price variability modelling?

## Slide 5: AMIRIS Agent-based electricity market simulation
Fundamental modelling
  electricity prices
  actor revenues
Policy influence
  curtailment
  storage dispatch
  prosumer behaviour

## Slide 6: AMIRIS Price formation
Marginal cost /(€/MWh)
Demand
Supply
Energy /(MWh)
ƞmin
ƞmax
Merit order
  Inflexible demand
  High-res supply bids
Bids
  Marginal cost = bid price
  Power blocks: type-specific
  Efficiencies interpolated

## Slide 7: AMIRIS Conventionals - marginal costs
fuel cost
CO2 price
block efficiencies
other variable cost
marginal cost
power blocks
Not considered
  Control power markets
  Individual power plants
  Start-up cost
  Heat constraints
  …

## Slide 8: AMIRIS Resulting price
 Consider missing effects … but how?

## Slide 9: Hybrid approach Add markups & markdowns
Marginal cost /(€/MWh)
Energy /(MWh)
ƞmin
ƞmax
Bids /(€/MWh)
Energy /(MWh)
markup
markdown
 Fit markup & markdown values

## Slide 10: Markup determination Genetic algorithm
Nuclear
Coal
Gas CC
Gene pool
min max
AMIRIS
evaluate
fitness
Generation
X
X
X
kill weak
procreate
mutate
 Fit to price data 2012 – 2014

## Slide 11: Markup determination Validation
Descriptive statistics | Value
Pearson correlation | 0.86
Mean average error /€/MWh | 4.91
Root mean square error /€/MWh | 6.82
Validation with price data 2015 – 2016

 almost forecast level
 good variability
 slightly too low
 deep minima
 high peaks
 slightly overestimated
Price optimisation criterion | Target | Model
Standard deviation /€/MWh | 12.64 | 11.68
Mean /€/MWh | 30.30 | 28.37
Minimum /€/MWh | -130.09 | -46.78
Maximum /€/MWh | 104.96 | 83.75
Hours with negative prices | 223 | 366

## Slide 12: Markups Results
 Good stylized facts replication
Good replication of low prices
Slightly too low price level
 Consequences for storage?

## Slide 13: Impact on storage Dispatch & Surplus
Storage Parameters
2.5 GW
E2P = 5 12.5 GWh
 | Discharge hours /(h/a) | Discharged energy /(GWh/a) | Charge hours /(h/a) | Charged energy /(GWh/a)
No markups | 1,719 | 2,438 | 1,994 | 3,009
With markups | 2,570 | 3,318 | 2,628 | 4,097
 | Surplus /(k€/MWa)
No markups | 20.5
With markups | 16.9
With markups: More dispatch, ok,
but why less surplus?

## Slide 14: Markups Results
Data 2015 – 2016
no markups
markups
Markups improve shape parameters
More precise profitability estimates

## Slide 15: Impact of storage Price feedback
E2P = 5
Storage dampens price variability
 Verify storage dispatch

## Slide 16: Storage dispatch Model vs. data
E2P = 5 2 GW
Markups: better stylised facts of dispatch
Markups: higher correlation to measured dispatch

## Slide 17: Wrap up
Price variability
good reproduction necessary
fundamental modelling: complex
 hybrid approach: markups
Markups
fitted via genetic algorithm
price: better reproduction of stylised facts
room for improvement
Future work
include AT & LU
connect neighbouring market zones
improve storage dispatch algorithm
fundamental markup / bid modelling?
Application to storage
markups: better dispatch correlation
more precise surplus assessment