## Slide 1: Introduction to light-microscopy
Illustrated with widefield microscopy
Laurent Thomas - 2022

## Slide 2: Scale of observable objects
Notes: Electron microscopy higher resolution but fixed sample and complex sample preparation
Advantage of light microscopy live and fixed samples

## Slide 3: Widefield microscope – brightfield illumination / transmitted light
From ThermoFisher – Molecular Probes School of Fluorescence (MPSF)

## Slide 4: Up-right / Inverted microscopes
Notes: Inverted is more convenient for biology (petri dish…)
Orientation of a microscopy slide is important on an inverted -> also inverted i.e the coverslip below !

## Slide 5: Inverted microscope – transmitted-light path

## Slide 6: Widefield microscopy – Contrast methods
Biological samples are often transparent
AND/OR
Substructures are not distinguishable
Contrast methods are used to reveal these structures, organelles…
From Micron Course 2017 Oxford
Optical contrasting with transmitted light (DIC, Phase contrast…)
From ThermoFisher – MPSF
Sample contrasting by fluorescence labelling

## Slide 7: Contrasting methods – transmitted light
- Chemical staining with classical brightfield illumination
Ex : H&E staining in histochemistry
H&E staining from wellcomecollection.org
Using a filter to “color” the transmitted light can help emphasizing absorbing structures
principle of light-absorption as in Beer-Lambert law
Darkfield
only light deviated/diffracted by the sample is collected
Phase-contrast
Transform the phase shift of the light (from tissues with different refraction indexes) to a difference of intensity
DIC
turns the difference of optical path into a difference of polarization to create contrast
Polarised illumination (ex: for geology)
(DIC)
From Micron Course 2017 Oxford
Notes: Staining : Take advantage of affinity with a dye (need fixing though + preparation)
Turns the physical difference, resulting in a phase difference into difference of contrast

## Slide 8: Contrast method – Fluorescence emission
The sample is labelled with a fluorescent molecule (protein, dye…),
contrast is achieved by exciting the fluorophores (with light), and imaging the light they emit
Both excitation/emission happens simultaneously
(at the sample level, not molecular)
i.e emitted fluorescence light is imaged while exciting
Notes: Contrary to transmitted light, not emitted light
Dichroic mirror needed to have both excitation and emission through the objective

## Slide 9: Fluorescence excitation/emission Perrin-Jablonski diagram
As the energy E decreases, lambda increases
i.e shift from blue toward red, so-called “Stokes-shift”
The cycle absorption/emission is very fast (ns range) and is repeated for a given number of cycles, after which the fluorophore is “bleached”
constant

## Slide 10: Absorption/emission spectrum
Absorption spectrum (for excitation)
Emission spectrum
Notes: Specific for each fluorescent molecule
Stokes shift taken advantage of for the dichroic

## Slide 11: Objective and resolution
The objective numerical aperture (NA) influences the resolution and the size of the field of view.
The higher the numerical aperture, the higher the resolution, but the smaller the field of view.
Working distance
Two 6 µm beads imaged at 4, 10 and 40X magnification
From ThermoFisher - Molecular Probes School of Fluorescence
Abbe´s diffraction law, for lateral (XY) resolution
With dmin the smallest distance which can be distinguished (ex : between 2 points)
Super-resolution methods exist to work around this limit, using image-reconstruction…

## Slide 12: Resolution and diffraction limit
All optical systems are limited by the diffraction of light.
The image of a spot is a diffraction-limited spot.
The image formation is obtained by convolution of the object with the Point-Spread Function (PSF) of the system
PSF
From Micron course 2017
Oxford

## Slide 13: Optical aberrations
Photon diffusion/scattering (thick specimen)
Large specimen are composed of complex heterogeneous tissues which cause diffusion/scattering of the photons within the sample, degrading the image-quality (blur).
Optical components are not perfect
Chromatic aberrations are “systematic” and can/should be corrected (using multi-color beads), especially for multi-colour imaging/colocalization
From Micron Course 2017 Oxford
Favre-Bulle, Itia & Stilgoe, Alexander & Scott, Ethan & Rubinsztein-Dunlop, Halina. (2019). Optical trapping in vivo: Theory, practice, and applications. Nanophotonics. 8. 10.1515/nanoph-2019-0055.

## Slide 14: Immersion objectives (water/oil)
Oil immersion is used to remove one interface,
preventing refractive index mismatch causing aberrations.
The oil has the same refractive index than the glass.

## Slide 15: Widefield microscopy – Pros and Cons
Pros | Cons
Simple setup (compared to other techniques) | Limited contrast : background fluorescence from widefield illumination
Fast imaging | 
Low photo-toxicity (no laser) | 
Reproduced from
Moran-Mirabal, Jose. (2013). Advanced-Microscopy Techniques for the Characterization of Cellulose Structure and Cellulose-Cellulase Interactions *. 10.5772/56584.
Deconvolution can be used to improve signal-to-background :
reversing the image-formation process (i.e reversing the convolution with the PSF)
BUT complex computational method !
Image by Marco Campinho, Universidade do Algarve and Claudia Florindo - Andor Technology

## Slide 16: Other techniques
Each technique has its own pro/cons
Confocal (better signal-to-background)
Spinning disk (better signal-to-background + fast)
TIRF (better signal to background)
Structured Illumination (higher resolution)
Single-Plane Illumination Microscopy (SPIM) / Light-sheet (fast and large volume)
Super-resolution (STED, STED/PALM) : single-molecule resolution but slow
Etc…
Sample health / Photo-toxicity
Temporal
resolution
Signal-to-noise
ratio
Spatial
resolution
For any technique, prioritizing one summit of the pyramid…
means sacrificing the others
Notes: Ex : more temporal resolution (more often imaging) = more phototoxicity
Higher laser power = better signal to background but phototxicity too

## Slide 17: Resources
Manufacturers' resources
Nikon MicroscopyU https://www.microscopyu.com/
Molecular Probes School of Fluorescence | Thermo Fisher Scientific – DE
Microscopy Resource Center | Olympus LS (olympus-lifescience.com)
Scientific and educational portal for microscopy | Science Lab | Leica Microsystems (leica-microsystems.com)
Community resources
Overview of Microscopy Techniques: Confocal, Widefield, Transmitted Light and Deconvolution (biologists.com)
Microlist – Microscopy courses, software, meetings & jobs
Oxford Micron Course (2017) - Index of /lectures/micron_course_2017 (ox.ac.uk)
Oxford Micron Course (2019 and on) - micron-facility/micron-course-2019 (github.com)
iBiology YouTube channel
Microforum - Light microscopy forum (microlist.org)
ImageInLife MOOC series – Week 3 : Microscopy
https://youtube.com/playlist?list=PL7149X9aKjLF_bbOEa1osyqDlFvzyYW25

## Slide 18: Acknowledgements
Most illustrations in this presentation are extracted from the ThermoFisher Molecular Probes School of Fluorescence educator packet.
The images and figures in the educator packet are copyrighted, but they are freely available for use as long as the attribution “Molecular Probes™” remains intact.
A significant fraction of illustrations also comes from the course material of the Micron Facility in Oxford, which slides are available online (see previous Resource slide).