## Slide 1: Control and Automation of Production Systems Ingeniería Industrial Master's Degree
Unit 7:
ST Programming
Notes: Para añadir librerías a codesys
Abra el administrador de librerías en:
‘Ventana’, ‘Administrador de librerías’,
Se abre una ventana (posiblemente vacía pues no hay librerias), en la parte superior, izquierda (Que sale un espacio blanco marcado en azul), le das con el botón derecho
‘insertar’, ‘otras bibliotecas….’ seleccionamos la standard.lib

## Slide 2: ST Programming
High level programming language
  C, Matlab, Java, Pearl…
Appropriate language to manage non-boolean information/data
  Integers (count)
  Real numbers (PID control, time/date management)
  Vectors and matrices (stock or list management)
  Character strings (text messages and history management)
Objective
  To create a sub-system programmed in ST in order to manage this type of information. It must be able to interact with other POUs
    CTUD or TON

## Slide 3: Types of data
Boolean
  BOOL, BYTE, WORD, DWORD, LWORD
Integers
  Signed: INT, SINT, DINT, LINT
  Unsigned: UINT, USINT, UDINT, ULINT
Real numbers
  REAL, LREAL
Character strings
  STRING
Time
  TIME, DATE, TIME_OF_DAY, DATE_AND_TIME
VAR
Height: INT:=0;
Increment: INT:=1;
END_VAR

## Slide 4: Types of data
1Dimension array (vectors)
  Declaration
    <name> : ARRAY OF [1..<size>] OF <type>;
  Assignment
    <name> [<pos>] := <value>;
>1Dimension array (Matrices)
  Declaration
    <name> : ARRAY OF [1..<row>,1..<col>] OF <type>;
  Assignment
    <name> [<row>,<col>] := <value>;
VAR
j : INT;
Vector : ARRAY [0..10] OF BOOL;
Matrix : ARRAY[1..20,2..100] OF INT;
Cx:ARRAY [0…6] OF INT:= 1,2,3,4,5,6,7 ; (*initial values*)
M: ARRAY [1..2,3..4] OF INT := 1,3(7); (* 1,7,7,7 *)
END_VAR (*See Codesys help*)
Vector[3] := 4;
Matrix[17,45] := 10;
Vector[3*j] := 5*j;
Notes: ¿LA PRIMERA COMPONENTE ES LA CERO O LA 1? O LO PUEDO DECIDIR YO?
Parece que lo puedes decidir tu.
Ejemplos de inicialización completa de un array
Cx:ARRAY [0…6] OF INT:= 1,2,3,4,5,6,7 ;
M: ARRAY[1..2,3..4] OF INT := 1,3(7); (*Abreviatura de 1,7,7,7 *)
[] Brackets
() braquets or parenthesis
{} curly brackets

## Slide 5: Data representation
BOOL: x:=TRUE
BYTE: X:=16#5F (hex.)
X:=2#0101_1111 (bin)
STRING: NAME:=‘AGV3’;
TIME: TFIN:=T#2d3h34m19s34.5ms;
DATE: DFIN:=D#2014-06-10;
TIME_OF_DAY: HFIN:=TOD#13:23:45:44;
DATE_AND_TIME:
DFIN:=DT#2013-10-09-13:23:45:44;

## Slide 6: Derived data
They allow to define non-elementary data, as vectors, matrices or structures
TYPE MyReal : LREAL; Color : (red, yellow, green) ; (* Numbered type*) Sensor : INT (-128..128); (*Integer with range*) Measure1D : ARRAY [1..45] OF Sensor; (*Vectors*) Measure2D : ARRAY [1..45,1..45] OF REAL; (*Matrix*) MyStructure: STRUCT Value: INT; Measure1 : Measurement1D; Light : Color; END_STRUCT; END_TYPE

## Slide 7: ST Programming
Expressions
  Set of operators, variables and constants
  Expressions yield a value of a certain type
    Used in assignments
    Logical conditions (boolean type)
Operators
  (),+,-,*,**,/,MOD,>,>=,<,<=,=,<>,&,AND,OR,XOR,NOT
Notes: MIRAR EN EL LIBRO DE MIGUEL ANGEL, QUE DIFERENCIA HAY ENTRE & Y AND, QUE ES **
= es comparación
Parece que & y AND es lo mismo
** es exponencial

## Slide 8: ST Programming
ST program
  Ordered set of statements
  Execution of all statements one time per automation cycle
  Comments (*….*)
ST statement
  Assignment
    Changes the value of a variable
    <name> := <expression>;
  Flow control
    Branches (IF, CASE)
    Loops (WHILE, FOR)
FCI1:=FALSE;
FCD1:=FALSE;
IF MOTOR_DE1=TRUE THEN
PosX1:=PosX1+Vel1;
END_IF
Notes: : Colon

## Slide 9: ST Programming
Branches
  IF…THEN…ELSEIF…. THEN… ELSE…END_IF
  CASE...OF...END_CASE
Notes: SUB? ADD? MUL? DIV? A Y B SON VECTORES?
Son funciones , se verán en el siguiente tema

## Slide 10: ST Programming
Loops
  FOR...TO...BY...DO...END_FOR
  WHILE...DO...END_WHILE
  REPEAT...UNTIL...END_REPEAT

## Slide 11: Example
CTUD counter
Global variables
Edge triggering
ST Programming

## Slide 12: Example
CTUD counter
VAR_GLOBAL
CU: BOOL;
CD: BOOL;
Reset: BOOL;
Load: BOOL;
PV: INT;
QU: BOOL;
QD: BOOL;
XV: INT;
END_VAR
PROGRAM MICTUD
VAR
CUa: BOOL;
CDa: BOOL;
Reseta: BOOL;
Loada: BOOL;
END_VAR
IF Load=1 AND Loada=0 THEN
XV := PV;
END_IF
Loada := Load;
IF Reset=1 AND Reseta=0 THEN
XV := 0;
END_IF
Reseta := Reset;
IF CU=1 AND CUa=0 THEN
XV := XV+1;
END_IF
CUa := CU;
IF CD=1 AND CDa=0 THEN
XV := XV-1;
END_IF
CDa := CD;
IF XV >= PV THEN
QU := 1;
ELSE
QU := 0;
END_IF
IF XV <= 0 THEN
QD := 1;
ELSE
QD := 0;
END_IF
Notes: Common errors:
Not writing ELSE in the output assignment (blocking number 1)
IF XV >= PV THEN
QU := 1;
END_IF
IF XV <= 0 THEN
QD := 1;
END_IF
Incorrect use of WHILE
WHILE XV < PV
QU := 0;
END_WHILE

## Slide 13: Example
CTUD counter

## Slide 14: ST Programming
It is possible to program any LD/Petri net in ST
  It is not the most appropriate tool
Using ST to program procedures with non-boolean information
  Isolating the information management in a sub-system that can communicate with the rest
IF NOT Linf THEN
Valvula1 :=1;
END_IF
IF LSup THEN
Valvula1 :=0;
END_IF
Valvula2 := Fmezcla;
Notes: Decir que se puede hacer todo pero que hay que intentar usar el lenguaje apropiado
Cualquier sentencia LD se puede poner en ST
Cualquier RdP se puede programar de forma sistemática en ST (no lo vamos a ver)

## Slide 15: Using ST in Petri nets
ST statements in Petri nets
  Management of non-boolean variables
Boolean expressions
  Logical condition of transition
State assignments
  The assignment is executed in each cycle!
Start
V
height>10
MD, state:=7;
FCD
VV, state:=8;
height<0
MI
FCI

## Slide 16: Using ST in SFC (Codesys)
Transitions
  They allow to introduce an expression directly in ST
Place assignments
  Add an action in POU SFC
  Link an action
    Name the action
  The code is execute one time per cycle in which the place is active

## Slide 17: ST programming
Function calling
  Function: A:=XOR(B,C)
Function block calling
VAR
IT: BOOL;
FT:BOOL;
TIEMPO: TIME;
TEMP: TON;
END_VAR
-------------
TEMP.IN:=IT;
TEMP.PT:=T#15s;
TEMP();
FT:=TEMP.Q;
TIEMPO:=TEMP.ET;
VAR
IT: BOOL;
FT:BOOL;
TIEMPO: TIME;
TEMP: TON;
END_VAR
-------------
TEMP(IN:=IT, PT:=T#15S,ET=>TIEMPO, Q=> FT);
TIMER CALLS
PASARLO AL SIGUIENTE TEMA

## Slide 18: Example
VAR
IT: BOOL;
FT:BOOL;
TIEMPO: TIME;
TEMP: TON;
CONT: INT:=0;
END_VAR
---------------
IF FT=FALSE THEN
IT:=TRUE;
ELSE
CONT:=CONT +1;
IT:=FALSE;
END_IF;
TEMP(IN:=IT, PT:=T#3S, ET=>TIEMPO, Q=>FT);
COUNTER WITH INCREMENTS EVERY 3 SECONDS
PASARLO AL SIGUIENTE TEMA