## Slide 1: PILOT 5. Biosolvents

## Slide 2: Pilot 5. Biosolvents
Place | Athens, Greece
Responsible partner | National Technical University of Athens
Type of feedstock | Source-separated biowaste
Responsible partner for feedstock provision | Sustainable City
Process | Saccharification and fermentation
Responsible partner for process development | National Technical University of Athens
End-product | Bioethanol
Responsible partner for end-product development | National Technical University of Athens
Treatment Capacity | 50 kg dried biowaste/operational cycle

## Slide 3: Utilisation of separated biowaste for bio-based-chemicals (PILOT 5: Biosolvents)
Feedstock supply and logistics
Optimization phase: Corrective and adjustment actions in order to ensure that the actual equipment and bioprocess will successfully operate with the urban biowaste form Greece at optimum yields
1st operation period: Continuous operation (over 10 operating cycles) of the pilot plant with dried biowaste
2nd operation period: Continuous operation (over 10 operating cycles) of the pilot plant with real feedstock – wet separately collected biowaste

## Slide 4: Feedstock supply, logistics
Feedstock supplier: Households of Vari-Voula- Vouliagmeni (VVV) Municipality
Feedstock collection and transportation to Pilot 5: Cleaning service of the Municipality of VVV
Delivery Frequency: 15 days (Tuesday, 6 am)

## Slide 5: Optimisation period for biosolvents production

## Slide 6: Characterization of substrate for lactic acid production
Parameter | Value (% d.b.)
Total Solids | 99.2 ± 0.4
Moisture | 0.8 ± 0.4
Volatile Solids | 96.1 ± 0.0
Ash | 3.9 ± 0.0
Oils | 2.5 ± 0.1
Water-Soluble Solids | 36.2 ± 1.0
Starch | 39.8 ± 0.2
Insoluble Acid Residue | 7.5 ± 0.4
Lactose | 19.1 ± 2.3
Free Glucose | 1.1 ± 0.1
Biowaste stream rich in starch and lactose.
Lactic Acid Bacteria

## Slide 7: Simultaneous Saccharification and Fermentation for Lactic Acid production
Effect of lactase
Parameter | Trial 1 | Trial 2
Lactozyme Pure (mg /gLactose) | 5 | 20
Spirizyme Excel XHS (μL/gStarch) | 40 | 40
Inoculum size (% v/v) | 5 | 5
Solid loading (% w/w | 10 | 10
Temperature (℃) | 35 | 35
Chart: Time (h)
| 24 | 48 | 144 | 168 | 216 | 288
Low lactase level | 6.195 | 13.315 | 13.4 | 14.96 | 14.825 | 15.965
High lactase level | 6.585 | 9.71 | 10.64 | 11.59 | 14.725 | 16.7

## Slide 8: Simultaneous Saccharification and Fermentation for Lactic Acid production
Effect of inoculum size
Parameter | Trial 1 | Trial 2
Lactozyme Pure (mg /gLactose) | 5 | 5
Spirizyme Excel XHS (μL/gStarch) | 40 | 40
Inoculum size (% v/v) | 5 | 10
Solid loading (% w/w | 10 | 10
Temperature (℃) | 35 | 35
Chart: Time (h)
| 24 | 48 | 120 | 144 | 168 | 216 | 288
Low inoculum size | 6.195 | 13.315 | 13.4 | 13.4 | 14.96 | 14.825 | 15.965
High inoculum size | 6.1 | 8.75 | 16.685 | 17.29 | 17.5 | 17.4 | 17.8

## Slide 9: Repeated Fermentation for Lactic Acid production
Trial 1
Run | 1 | 2 | 3 | 4 | 5
Productivity (g/L h) | 0.18 ± 0.0 | 0.23 ± 0.0 | 0.30 ± 0.0 | 0.31 ± 0.0 | 0.29 ± 0.0

## Slide 10: Repeated Fermentation for Lactic Acid production
Trial 2
Run | 1 | 2 | 3 | 4 | 5
Productivity (g/L h) | 0.18 ± 0.0 | 0.23 ± 0.0 | 0.38 ± 0.0 | 0.35 ± 0.0 | 0.38 ± 0.0

## Slide 11: Repeated Fermentation for Lactic Acid production
Trial 3
Run | 1 | 2 | 3 | 4 | 5
Productivity (g/L h) | 0.18 ± 0.0 | 0.21 ± 0.0 | 0.39 ± 0.0 | 0.40 ± 0.0 | 0.95 ± 0.0

## Slide 12: Ethyl lactate production at liquid phase
Parameter | Trial 1 | Trial 2 | Trial 3
Lactic acid (%w/w) | 80 | 88 | 88
Bioethanol (%v/v) | 99 | 99 | 89
Temperature (℃) | 100 | 100 | 100
wcat | 0.1 | 0.1 | 0.1
Molar ratio (nEthanol/nLacticAcid) | 3/1 | 3/1 | 3/1

## Slide 13: Ethyl lactate production at liquid phase
Chart: Time (min)
| 0 | 30 | 60 | 135 | 195 | 255
Lactic acid 80% w/w | 0 | 2.9047 | 3.6278 | 44.4714 | 40.9432 | 59.8466
Lactic acid 88% w/w | 0 | 23.4658 | 33.4214 | 38.3584 | 57.4511
Chart: Time (min)
| 0 | 30 | 90 | 150 | 210 | 270
Bioethanol 89% v/v | 0 | 2.3814 | 10.8098 | 11.7098 | 29.1192 | 54.0145
Bioethanol 99 % v/v | 0 | 23.4658 | 33.4214 | 38.3584 | 57.4511

## Slide 14: Ethyl lactate production with reactive distillation
 | Ethanol from Pilot 5 | Ethyl lactate produced by TBWR | Commercial ethyl lactate
Feedstock origin | Pilot 5 - NTUA | Pilot 5 - NTUA | -
Purification method | - | Vacuum distillation | -
Physical state | liquid | liquid | liquid
Color | clear | clear | clear
Smell | Smell of biowaste | neutral | fruity
Purity (HPLC) | - | >96% | >96%
Density (kg/L) (24°C) | 0.794 | 1.024 | 1.030
Refractive index (20°C) | 1.362 | 1.413 | 1.413

## Slide 15: Demonstration of the utilisation of dried source separated biowaste for the production of bioethanol

## Slide 16
Operational Conditions
Parameter | 
Feedstock | Dried
Amylase (μL/g starch) | 40
Cellulase (μL/g cellulose) | 175
Yeast (%) | 2
Fermentation mode | SSF
Solid Loading (%) | 25
Continuous operation (over 10 operating cycles) of the pilot plant with dried biowaste

## Slide 17
Interior of Reactor:
Characteristics:
Two rotating vessels
Double walls
Temperature control with water
Controlled by PLC
PLC:
Hydrolysis - Fermentation

## Slide 18
Distillation - Dehydration
Distillation Unit:
70 oC
Vacuum pump
1st Distillate:
35 % v/v
Lab-scale two stage distillation: 94-95 % v/v
Zeolite 3A:
99,55 % v/v

## Slide 19: Results

## Slide 20: Results (cont.)

## Slide 21: Results
Ethanol (L/tn dried FW) | 135.34±16.35
Ethanol yield (%) | 86.60±4.91
Chart: Trial
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Ethanol yield (%) | 87.46 | 58.11 | 89.011 | 73.9217 | 86.2314 | 91.4493 | 89.3196 | 85.8618 | 90.6974 | 89.5444 | 91.032 | 87.545 | 82.0293 | 81.7243
Ethanol (L/tn dried FW) | 131.7871 | 77.5665 | 152.324 | 146.2993 | 159.3135 | 113.0734 | 136.8821 | 114.0684 | 133.4 | 143.2663 | 145.9777 | 152.0913 | 113.0345 | 117.8707

## Slide 22: 1st operation period
 | Trial 1 | Trial 2 | Trial 3 | Trial 4 | Trial 5 | Trial 6 | Trial 7 | Trial 8
Solid Degradation (%) | 46.28 | 46.43 | 63.86 | 70.20 | 67.96 | 64.27 | 68.54 | 65.74
Cellulose Degradation (%) | 73.61 | 38.84 | 74.27 | 88.31 | 78.78 | 72.48 | 82.33 | 71.10
Starch Degradation (%) | 89.46 | 95.36 | 92.43 | 95.17 | 95.65 | 95.85 | 90.77 | 83.18
 | Trial 9 | Trial 10 | Trial 11 | Trial 12 | Trial 13 | Trial 14 | Mean Value |  | 
Solid Degradation (%) | 67.76 | 68.78 | 65.45 | 65.26 | 68.12 | 64.47 | 63.79 | ± | 7.64
Cellulose Degradation (%) | 68.86 | 75.57 | 75.98 | 77.54 | 80.27 | 81.71 | 76.80 | ± | 5.22
Starch Degradation (%) | 96.37 | 93.42 | 96.06 | 96.39 | 95.76 | 96.89 | 94.57 | ± | 2.35

## Slide 23: Energy consumption
Main stages of the process:
drying
simultaneous saccharification and fermentation process
final recovery of produced ethanol via distillation
GAIA dryer GC-100:
0.66kWh/kg wet feedstock
2.46kWh/kg dried feedstock

## Slide 24: Energy consumption
Conditions Time (h) | Temperature (οC) | Stirring Rate (%) | Stirring Time (min/h) | Energy (kWh/kg dried feedstock)
0 - 8 | 35 | 35 | 40 | 0,24
9 - 24 | 35 | 20 | 25 | 0,44
Heating and mixing conditions applied during SSF pilot trials
Distillation energy needs: 12.83kWh/L ethanol

## Slide 25: Energy consumption
Chart: 
| Drying | Bioconversion | Distillation
Energy consumption | 49.2 | 13.6 | 36.6

## Slide 26: Demonstration of the utilisation of wet source separated biowaste for the production of bioethanol

## Slide 27: Experimental Conditions
Enzymes and Yeast :
Amylase: 40μL/g starch
Cellulase : 175μL/g cellulose
S. Cerevisiae 2% w/w d.b.
Average Composition
Starch: 7% w/w d.b
Cellulose: 14% w/w d.b
Moisture: 75%
Process: Simultaneous Saccharification and Fermentation (SSF)
Temperature: 35 oC
Time: 24 Hours
Solid Loading: 10 - 15 % w/w

## Slide 28
Feedstock Pretreatment
Shredder Bowl Cutter LFC-18V2
15 min milling and homogenization per 15kg of fresh biowaste
Fresh Food Waste
Milled and Homogenized Food Waste
Moisture ~ 75%
Moisture ~ 75%

## Slide 29
Characteristics:
Two rotating vessels
Double walls
Temperature control with water
Controlled by PLC
Hydrolysis - Fermentation

## Slide 30
Distillation - Dehydration
Distillation Unit:
70 oC
Vacuum pump
1st Distillate:
35 % v/v
Lab-scale two stage distillation: 94-95 % v/v
Zeolite 3A:
99.55 % v/v

## Slide 31: Results

## Slide 32: Results (cont.)

## Slide 33: Results
Ethanol (L/tn dried FW) | 133.42 ± 33.42
Ethanol yield (%) | 74.05 ± 6.82
Chart: Trials
Ethanol Yield (%) | 0.62118 | 0.79397 | 0.67562 | 0.69985 | 0.69329 | 0.71449 | 0.75122 | 0.70212 | 0.8526 | 0.75612 | 0.88545
Ethanol (L/(tn FW solid)) | 98.3789 | 111.8461 | 164.5504 | 119.7686 | 157.4778 | 101.3454 | 106.5115 | 102.9103 | 205.51 | 134.6501 | 164.7182

## Slide 34: Results
 | Trial 1 | Trial 2 | Trial 3 | Trial 4 | Trial 5 | Trial 6
Solid Degradation (%) | 75.13 | 85.13 | 57.84 | 68.66 | 58.83 | 45.22
Starch Degradation (%) | 79.29 | 89.87 | 47.26 | 55.40 | 90.15 | 30.67
Cellulose Degradation (%) | 88.87 | 94.51 | 63.04 | 72.44 | 71.85 | 57.84
 | Trial 7 | Trial 8 | Trial 9 | Trial 10 | Trial 11 | Mean Value |  | 
Solid Degradation (%) | 54.44 | 50.39 | 66.39 | 63.09 | 72.33 | 63.40 | ± | 12.60
Starch Degradation (%) | 87.06 | 88.83 | 97.12 | 83.00 | 88.95 | 76.15 | ± | 23.46
Cellulose Degradation (%) | 76.38 | 69.33 | 90.94 | 83.94 | 82.80 | 77.45 | ± | 12.77

## Slide 35: Energy consumption
Main stages of the process:
shredding
simultaneous saccharification and fermentation process
final recovery of produced ethanol via distillation
Shredder Bowl Cutter LFC-18V2:
0.035±0.005 kWh/kg wet feedstock
0.187±0.03 kWh/kg dry feedstock
Distillation energy needs
Heating and mixing conditions applied during SSF pilot trials
0.25±0.06 kWh/kg wet feedstock
1.05±0.24 kWh/kg dry feedstock
6.94 kWh/L ethanol

## Slide 36: Energy consumption
Chart: 
| Shredding | Bioconversion | Distillation
Energy consumption | 8.64 | 48.19 | 43.17
2.17kWh per kg of dried feedstock
0.52kWh per kg of wet feedstock
16.07 kWh per L of ethanol produced

## Slide 37: Comparison of dried and wet source separated biowaste as feedstock for bioethanol production

## Slide 38: Operational conditions
The same consumption of enzymes and yeast
The same fermentation mode (SSF)
(Un)known composition of feedstock
Different solid loading
Lower loading  Larger reactor volumes  Higher CAPEX

## Slide 39: Ethanol yields of the operational phases
 | Dried feedstock | Wet feedstock
Ethanol yield (%) | 86.60±4.91 | 74.05 ± 6.82
Ethanol yield (L/tn dried feedstock) | 135.33±16.35 | 133.42 ± 33.42
Ethanol (L/tn feedstock as received) | 33.72±5.29 | 24.75 ± 7.09

## Slide 40: Degradation efficiencies of the operational phases
Degradation Efficiency (%) | Dried feedstock | Wet feedstock
Total Solids | 63.79 ± 7.64 | 63.40±12.60
Starch | 94.60 ± 2.40 | 80.69±16.27
Cellulose | 76.80 ± 5.20 | 79.41±10.37

## Slide 41: Energy consumption of the operational phases
 | Dried feedstock | Wet feedstock
Total energy consumption (kWh/kg dried feedstock) | 4.25±0.24 | 2.17±0.38
Total energy consumption (kWh/kg wet feedstock as received) | 1.11 ±0.05 | 0.52±0.09
Total energy consumption (kWh/L ethanol produced) | 32.11 ± 4.02 | 16.07 ± 2.85
Pretreatment (%) | 61.28 | 8.64
Bioconversion (%) | 13.21 | 48.19
Distillation (%) | 25.51 | 43.17

## Slide 42: Energy consumption of the operational phases
Chart: Energy Consumption (kwh/kg Wet Feedstock)
| 2nd Phase Dried Feedstock | 3rd Phase Wet Feedstock
Pretreatment | 0.674 | 0.045
Bioconversion | 0.145 | 0.25
Distillation | 0.28 | 0.22
Dried Feedstock
Wet Feedstock