## Slide 1
Trying an IP Over NDN Packet Gateway
Marielena Márquez-Barreiro
Miguel Rodríguez-Pérez
Sergio Herrería-Alonso
Notes: 1

## Slide 2
Information Centric Networking
2

## Slide 3
Named Data Networking
NDN does not address nodes, but content itself
Two network level PDUs: Interest and Data
⇒ Pull-based communication model
3
Named data
Named data
data
data
Data
Interest
CONSUMER
PRODUCER
data

## Slide 4
IP and NDN Coexistence
IP is currently being used as L2 layer in (some) NDN networks
Future NDN native networks will need to serve as L2 layer for legacy IP traffic
⇒ Tunneling IP traffic across NDN networks
Advantages?
NDN boasts native multicast, security and mobility characteristics
4

## Slide 5
Gateway Implementation: v1
5
Request name: /IP_DST_GATEWAY/ip/request/IP_SRC_GATEWAY/seqno
Claim name: /IP_SRC_GATEWAY/ip/datagram/seqno

## Slide 6
Gateway Implementation: v2
Packet Coalescing
6

## Slide 7
Experimental Setup
7

## Slide 8
Results
Caveats:
NFD used as router: not optimized for performance
Simulation on an overloaded laptop computer
8
 | v1 | v2 | Improvement
UDP Throughput | 0.71Mb/s | 1.04 Mb/s | 46%
TCP Throughput | 0.77 Mb/s | 1.48 Mb/s | 92%
UDP Jitter | 13.78 ms | 8.60 ms | 38%
UDP Loss Rate | 7.5 % | 0 % | 100%

## Slide 9
Conclusions
Proof-of-concept IP gateway on top of native NDN
Mismatches between push and pull models lead to lack of performance
Large room for improvement: simple modifications lead to much increased performance
Simple v2 version capable of transmitting real-time video traffic
Future work
  Extend gateway to enable transmission of IP multicast traffic
  Leverage NDN network to synchronize gateway tables
9

## Slide 10
/atlanTTic | @atlanTTic_
Thank you
www.atlanttic.uvigo.es
Notes: 10